## Slide 1: Internal Logic Analyzer Final presentation-part B
By: Moran Katz and Zvika Pery
Mentor: Moshe Porian
Dual-semester project
Spring 2012

## Slide 2: Agenda
Overview
Goals
Requirements
Architecture
Internal Logic Analyzer Core
Integration
Data Flow
Simulations
Working Systems
Problems & Solutions
What have we learned
Notes: מורן

## Slide 3: Project Overview
Altera- Signal Tap
Xilinx- Chip Scope
Logic Analyzer- Debugging tool for FPGA
Hardware: Change FPGA code
Memories to store data
Logic to change configuration
Common Logic Analyzer tools today:
Notes: 1.יצרניות ה- FPGA-ים מספקות כלי למטרת DEBUG במעבדה, הקרוי Logic Analyzer, המאפשר הקלטה של מידע פנימי ב- FPGA והצגתו למשתמש. הכלי בנוי מחבילת חומרה, וחבילת תוכנה.(תמונה)
2. החלק החומרתי נכנס לקוד של ה- FPGA וכולל זיכרונות לאחסון המידע המוקלט, לוגיקה לשינוי קונפיגורציה (לדוגמא: סוג ה- Trigger, לדוגמא: פעיל בשינוי מ- '0' ל- '1'), לוגיקה לזיהוי נעילה של ה- Trigger הרצוי ולוגיקה לשליחת המידע המוקלט לתוכנה.
3. הכלי של יצרנית ה- FPGA-ים, ALTERA, נקרא SignalTap. הכלי של יצרנית ה- FPGA-ים, XILINX, נקרא ChipScope.
מורן

## Slide 4: Project goals
XILINX- SPARTAN 3E
ALTERA- CYCLON II
Design an internal logic analyzer to the FPGA which will be an independent part
Hardware:
(1) VHDL
(2) Record the chosen signals
(3) Send it back to the user
Notes: בניית Logic Analyzer פנימי ל- FPGA, בלתי תלוי ביצרן ה- FPGA. החלק החומרתי יכלול בניית מערכת ב- VHDL, המאפשרת הקלטה של הסיגנלים הרצויים ע"פ קונפיגורציה ושליחת המידע המוקלט חזרה למשתמש. החלק התוכנתי יכלול בניית GUI המאפשר שינוי קונפיגורציה והצגת המידע המוקלט למשתמש. בנוסף, תבנה מערכת תומכת המאפשרת בדיקה של המימוש במעבדה.
מורן

## Slide 5: Requirements
Option to choose the parameters
Save the recorded information and present it using waveform
Internal communication is through Wishbone protocol
External communication is through UART protocol
Type of trigger, for example ‘rise’
position of trigger
30%-70%
50%-50%
70%-30%
Duration of recording
Notes: כלי ה- Logic Analyzer יהיה בעל תכונות המאפשרות:
  בחירת סוג ה- Trigger: שינוי מ- '0' ל- '1' (rise), fall, '0', '1'.
  בחירת מיקום ה- Trigger ביחס למידע המוקלט (באמצע, בהתחלה, בסוף...).
  קביעת כמות הסיגנלים להקלטה.
  קביעת עומק ההקלטה (זמן ההקלטה).
  שמירת וטעינת settings של פרויקט.
  שינוי שמות הסיגנלים המוצגים.
  שמירת המידע המוקלט לקובץ והצגתו באמצעות waveform בכלי סימולציה (ב- Modelsim).
  שימוש ב- Resources (זכרונות ולוגיקה) בלתי תלויים בסוג ה- FPGA.
כל הבלוקים ב- FPGA יקושרו ביניהם באמצעות ממשק אחיד – Protocol Wishbone.
הממשק ביו החומרה למשתמש ולתוכנה יהיה באמצעות פרוטוקול UART.
בניית מערכת תומכת, הכוללת חומרה ותוכנה, המאפשרת הזרקת חבילות מידע, המייצגות סצנות שונות של סיגנלים להקלטה ל- FPGA, קבלת מענה ממנו בנוגע למידע המוקלט והשוואה ביחס למצופה.
מורן

## Slide 6: Top Architecture
Altera Cyclone II
UART IN
RX PATH
WBM
OUTPUT BLOCK
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
USER
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Notes: מורן

## Slide 7: The Core
The core tasks:
Getting and saving user configurations
Getting new data each clock cycle and saving it
Getting new trigger signal each clock cycle and check for trigger rise according user configurations
Outputting relevant data back to user
The core is built from 7 entities:
WBS
Registers
Write Controller
RAM
Read Controller
Data Coordinator
WBM
Internal
Logic
Analyzer
Core
WBM
WBS
Notes: התמקדות ספציפית ברכיב הCORE, הרכיב המרכזי בפרויקט שמבצע את קליטת המידע והקונפיגורציות, שמירת המידע הרלוונטי והוצאתו בהתאם לקונפיגורציה.
שאר הרכיבים הם הרכיבים הסטנדרטיים שנמצאים בשימוש בפרויקטים
צביקה

## Slide 8: The Core
Description | Name | #
Generic table
1
2
3
4
5
6
7
8
9
10
11
12
reset_polarity_g
enable_polarity_g
signal_ram_depth_g
signal_ram_width_g
record_depth_g
data_width_g
Add_width_g
num_of_signals_g
power2_out_g
power_sign_g
type_d_g
len_d_g
0 - Reset active Low, 1- Reset active High
0 - Enable active Low, 1- Enable active High
depth of basic RAM
width of basic RAM
number of bits that is recorded from each signal
defines the width of the data lines of the system
width of address word in the RAM (Gets record_depth_g)
number of signals that will be recorded simultaneously
RAM output width is multiplied by this power factor
'-1' => RAM output width > input width
'1' => RAM input width > output width
Type Depth. type is the WB client which the data is directed to
Length of the WB data (in words)
Notes: צביקה

## Slide 9: Signal Generator
Signal
Generator
WBS
The signal generator tasks:
Generates every clock cycle data and trigger scene according user’s configurations
The signal generator was built in order to check the system and generate a scenes of data and triggers. at final state data and trigger should come from an external source
Notes: צביקה

## Slide 10: The Signal Generator
Description | Name | #
Generic table
1
2
3
4
5
6
7
8
9
10
reset_polarity_g
enable_polarity_g
data_width_g
Add_width_g
num_of_signals_g
external_en_g
scene_number_reg_1_address_g
type_d_g
len_d_g
0 - Reset active Low, 1- Reset active High
0 - Enable active Low, 1- Enable active High
defines the width of the data lines of the system
width of address word in the WB protocol
number of signals that will be recorded simultaneously
‘0’ => data generate in the entity
‘1’ => data input from external source
Address of scene number register
Type Depth. type is the WB client which the data is directed to
Length of the WB data (in words)
enable_reg_address_2_g
Address of enable register
Notes: צביקה

## Slide 11: Integration
Platform Changes:
Changing address width in all entities
Changing number, order and addresses of WhishBone entities and making them generics
Making Output Block inputs compatible to WB protocol
Notes: הצגת השינויים שבוצעו ברכיבים מפרויקטים אחרים: שינוי ראשון- רוחב הכתובת של המערכת וכל הישויות בה (קביעה כג'נריק). שינוי שני- התאמת רכיב OUTPUT_BLOCK והתאמתו ליציאת רכיב הCORE (חיבור בפרוטוקול WISHBONE)
צביקה

## Slide 12: Integration
Platform Changes:
Changing number, order and addresses of WhishBone entities and making them generics
At first the type of the entity that the data is send to was constant
Now the type is being written into a register and the entity read it from the register (we can write any type into the register)
Notes: התמקדות ספציפית בהפיכת המיספור של רכיבי הווישבון לגנריים על ידי שינוי בקוד הVHDL-> בהתחלה נכתב מידע לסלייב קבוע (type_in), ולאחר השינוי נכתב המידע שנשמר ברגיסטר
צביקה

## Slide 13: Data Flow
Trigger- first signal
Recording time- 50%
Signal’s number-2
injecting signals behavior
signal
signal
signal
Recorded data
Altera Cyclone II
Notes: שני שלבים לזרימת המידע:
קביעת קונפיגורציות: לדוגמא נבחר כטריגר סיגנל ראשון, עם עומק הקלטה של 50%. כמו כן נקבעת סוג הסצנה של רכיב הGENERATOR
המידע מתחיל לזרום מרכיב הGENERATOR אל הCORE, נקלט ונשמר ברכיב זה ולאחר מכן יוצא חזרה למשתמש דרך הTX
מורן

## Slide 14: Simulations
We made two different sets of simulations:
In the first set we created a Test Bunch to the whole system, and simulated different scenes and cases that the system could get
The second set simulated a read and write requests from all of the registers in the system
Notes: ביצענו שני סטים שונים של סימולציות: האחד למערכת כולה, והשני עבור קריאה וכתיבה לרגיסטרים של המערכת.
צביקה

## Slide 15: Simulations
At first we made a manual simulations to the core in order to check functionality
Afterwards, we built a top test bunch in order to check the entire system
Internal
Logic
Analyzer
Core
WBM
WBS
First set:
Notes: צביקה

## Slide 16: Simulations
Test plan first set:
Description | Test Number
Standard check, one block of output data | 1
Same as last, only scene number was changed | 2
Record depth is higher, other parameters are the same | 3
Evan higher record depth, but still one output block is generated | 4
We continue to enlarge the recording depth, and now the output data is divided into two data blocks (total recorded bits is larger then 1024) | 5
Two different recording scenes, one after another | 6
Writing to all of the registers in the entity at the same block | 7
Two different scenes, each one is written in one block | 8
Notes: צביקה

## Slide 17: Simulations
The same Test Bunch was used in both sets
A read and write scenes were made for all of the registers in order to check their functionality
Second set:
Notes: צביקה

## Slide 18: Simulations
Test plan second set:
Description | Test Number
Two write packs, and one read pack | 1
Two write packs, and one read pack (different registers) | 2
Three different packs to write, and one pack to read them all | 3
One pack to write for three registers, and one pack to read them all | 4
No write, two different packs to read two different registers (default values) | 5
Two write packs for five different registers, and two packs to read all those registers | 6
Notes: צביקה

## Slide 19: Synthesis
Initial synthesis was made to the whole system
Small bug fix was made
Notes: מורן

## Slide 20: Working Systems
File sharing- via SVN
Coding Guidelines- code design according known conventions, usage of entity template
Code Review- 1. Visual/ Compiler
            2. Local simulation to the entity
            3. Top simulation
Notes: מורן

## Slide 21: Problems & Solutions
Solution | Problem
Adding entity that “break” the data into few clock cycles (data coordinator) | Coordinate between number of recorded signals to output width (WB bus width)
Inserting wc_finish signal to the registers entity and resetting the relevant register after first trigger rise | Trigger was rise twice in the same configuration
We set each register size to 7 bit and we assume that the WB bus width is larger then that. According to that we read only the 7 LSB of the data into the registers | Coordinate between incoming data width (from WBS) to the registers
Coordinate addresses of incoming data and data sent to RAM | Coordinate between input - saved data and address. (couple of clock cycles delay between them)
Changing the TX PATH and making it generic to the WhishBone numbers | Numbers of whishbone slaves are determine in the entities, and not generics
Project stopped before we fix that. Core entity needs to be pipelined | System’s max clock rate is now 78 MHZ (suppose to be 100 MHZ)
Changing Output Block interface and making it WB suitable | Output Block inputs are not WB protocol suitable
Notes: צביקה

## Slide 22: Problems & Solutions
First example:
Output Block and Core interfaces are not match
Output Block inputs- Data in, Data in valid, Entity done
Core outputs- WBM compatible
NOT MATCH!!
Notes: צביקה

## Slide 23: Problems & Solutions
First example:
Our solution- Making changes in the Input Block inputs and making it compatible to WB protocol
Notes: צביקה

## Slide 24: Problems & Solutions
Second example: output width (bus) did not match the input width
DATA OUT
DATA OUT VALID
IN OUT COOARDINATOR
DATA OUT
DATA OUT VALID
Input width is num_of_signals_g, output width is data_width_g
Problem- the two widths don’t match
Our solution- adding an entity who coordinate between them
Notes: צביקה

## Slide 25: What have we learned
Planning and Specifying a Project
Integration to an existing platform
Protocols: UART, Wishbone
We expend our knowledge in VHDL
Usage of debugging tools for VHDL
Documentation, File sharing (SVN), Code Review, Presentation
Notes: מורן

## Slide 26: Next Stages
Completing synthesis
Integration with FPGA
Building a GUI
Lab checks
Final Lab debug
Notes: צביקה

## Slide 27: QUESTIONS
?