## Slide 1: Internal Logic Analyzer Final presentation-part A
By: Moran Katz and Zvika Pery
Mentor: Moshe Porian
Dual-semester project
Spring 2012

## Slide 2: Agenda
Overview
Goals
Requirements
Architecture
Data transfer
Internal Logic Analyzer Core
Registers
Write controller
Read controller
RAM
In out coordinator
Simulations
Problems & solutions
Part B work plan
Schedule

## Slide 3: Project Overview
Altera- Signal Tap
Xilinx- Chip Scope
Logic Analyzer- Debugging tool for FPGA
Contains software & hardware
Hardware: Change FPGA code
Memories to store data
Logic to change configuration
Software: Include GUI
Choose trigger, data location, signals name, record results
Common Logic Analyzer tools today:
Notes: 1.יצרניות ה- FPGA-ים מספקות כלי למטרת DEBUG במעבדה, הקרוי Logic Analyzer, המאפשר הקלטה של מידע פנימי ב- FPGA והצגתו למשתמש. הכלי בנוי מחבילת חומרה, וחבילת תוכנה.(תמונה)
2. החלק החומרתי נכנס לקוד של ה- FPGA וכולל זיכרונות לאחסון המידע המוקלט, לוגיקה לשינוי קונפיגורציה (לדוגמא: סוג ה- Trigger, לדוגמא: פעיל בשינוי מ- '0' ל- '1'), לוגיקה לזיהוי נעילה של ה- Trigger הרצוי ולוגיקה לשליחת המידע המוקלט לתוכנה.
3. החלק התוכנתי כולל GUI, המאפשר לבחור את סוג ה- Trigger להקלטה, מיקום ה- Trigger ביחס למידע המוקלט, הצגה נוחה של שמות הסיגנלים המוקלטים והצגה של תוצאות ההקלטה, המגיעות מהחומרה, למשתמש.
4. הכלי של יצרנית ה- FPGA-ים, ALTERA, נקרא SignalTap. הכלי של יצרנית ה- FPGA-ים, XILINX, נקרא ChipScope.

## Slide 4: Project goals
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Design an internal logic analyzer to the FPGA which will be an independent part
Hardware:
(1) VHDL
(2) Record the chosen signals
(3) Send it back to the user
Software:
(1) GUI- allow to present the recorded information
(2) Send request to change hardware according user’s choise
(3) Build a system to check our implementation
XILINX- SPARTAN 3E
ALTERA- CYCLON II
Altera Cyclone II
Notes: בניית Logic Analyzer פנימי ל- FPGA, בלתי תלוי ביצרן ה- FPGA. החלק החומרתי יכלול בניית מערכת ב- VHDL, המאפשרת הקלטה של הסיגנלים הרצויים ע"פ קונפיגורציה ושליחת המידע המוקלט חזרה למשתמש. החלק התוכנתי יכלול בניית GUI המאפשר שינוי קונפיגורציה והצגת המידע המוקלט למשתמש. בנוסף, תבנה מערכת תומכת המאפשרת בדיקה של המימוש במעבדה.

## Slide 5: Requirements
Save and load settings
Option to choose the parameters
Save the recorded information and present it using waveform
Internal communication is through Wishbone protocol
External communication is through UART protocol
Type of trigger, for example ‘rise’
Signals name, which signals to record
position of trigger
30%-70%
50%-50%
70%-30%
Duration of recording
Notes: כלי ה- Logic Analyzer יהיה בעל תכונות המאפשרות:
  בחירת סוג ה- Trigger: שינוי מ- '0' ל- '1' (rise), fall, '0', '1'.
  בחירת מיקום ה- Trigger ביחס למידע המוקלט (באמצע, בהתחלה, בסוף...).
  קביעת כמות הסיגנלים להקלטה.
  קביעת עומק ההקלטה (זמן ההקלטה).
  שמירת וטעינת settings של פרויקט.
  שינוי שמות הסיגנלים המוצגים.
  שמירת המידע המוקלט לקובץ והצגתו באמצעות waveform בכלי סימולציה (ב- Modelsim).
  שימוש ב- Resources (זכרונות ולוגיקה) בלתי תלויים בסוג ה- FPGA.
  אופציונאלי: הגדרת Trigger-ים חכמים, כמו Trigger מקונן (sequence של תנאים), Trigger הכולל השוואות לוגיות (greater than, לדוגמא).
כל הבלוקים ב- FPGA יקושרו ביניהם באמצעות ממשק אחיד – Protocol Wishbone.
הממשק ביו החומרה ל- GUI ולתוכנה יהיה באמצעות פרוטוקול UART.
בניית מערכת תומכת, הכוללת חומרה ותוכנה, המאפשרת הזרקת חבילות מידע, המייצגות סצנות שונות של סיגנלים להקלטה ל- FPGA, קבלת מענה ממנו בנוגע למידע המוקלט והשוואה ביחס למצופה.
הרחבה לגבי פרוטוקולי התקשורת תינתן בהמשך המצגת.

## Slide 6: Top Architecture
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Altera Cyclone II

## Slide 7: Data Transfer
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Trigger- first signal
Recording time- 50%
Signal’s number-2
injecting signals behavior
signal
signal
signal
Recorded data
Altera Cyclone II
Notes: קביעת קונפיגורציות: לדוגמא נבחר כטריגר סיגנל ראשון, עם עומק הקלטה של 50%

## Slide 8: The Core
The core tasks:
Getting and saving user configurations
Getting new data each clock cycle and saving it
Getting new trigger signal each clock cycle and check for trigger rise according user configurations
Outputting relevant data back to user
The core is build from 7 entities:
WBS
Registers
Write Controller
RAM
Read Controller
Data Coordinator
WBM

## Slide 9: The Core
Description | Name | #
Generic table
1
2
3
4
5
6
7
8
9
10
11
12
reset_polarity_g
enable_polarity_g
signal_ram_depth_g
signal_ram_width_g
record_depth_g
data_width_g
Add_width_g
num_of_signals_g
power2_out_g
power_sign_g
type_d_g
len_d_g
0 - Reset active Low, 1- Reset active High
0 - Enable active Low, 1- Enable active High
depth of basic RAM
width of basic RAM
number of bits that is recorded from each signal
defines the width of the data lines of the system
width of address word in the RAM (Gets record_depth_g)
number of signals that will be recorded simultaneously
RAM output width is multiplied by this power factor
'-1' => RAM output width > input width
'1' => RAM input width > output width
Type Depth. type is the WB client which the data is directed to
Length of the WB data (in words)

## Slide 10: Registers
Saves the user configurations
Sends out the configurations to the WC
configuration
POSITION
TYPE

## Slide 11: Registers
The inputs are Register’s address and data in
Valid signal rises and data in signal is being sampled to the relevant register according to the address
From now on, the data is available at the output
ADDRESS
DATA IN

## Slide 12: Write Controller
Gets the data from the signal generator and saves it in the RAM
Gets the trigger signal and looks for trigger rise according configurations
DATA IN
DATA IN VALID
ADDRESS
TRIGGER
TYPE
POSITION
START ADDRESS

## Slide 13: Write Controller
Trigger and data are entering each cycle
Data address and validity are being calculated and are being sent to the RAM
Trigger is compared to the configuration to identify trigger rise
If necessary start address is calculated according to the position and is being sent out
DATA IN
TRIGGER
AOUT VALID
ADDRESS
TYPE
?
POSITION
START ADDRESS

## Slide 14: Read Controller
Gets the start address from the WC
Extracting the relevant data from the RAM
Sends the data out to the in_out_coordinator
START ADDRESS
ADDRESS
DATA OUT
DATA VALID

## Slide 15: Read Controller
Start address is received
The next address is calculated and sent to the RAM
Data and validity is received from RAM
Output data is being sent to the coordinator
START ADDRESS
ADDRESS TO RAM
DATA VALID
DATA FROM RAM
DATA TO COORDINATOR

## Slide 16: In Out Coordinator
Gets data and valid in from Read Controller
Sends out the data and valid out to WBM
DATA
DATA VALID
DATA OUT VALID
DATA OUT

## Slide 17: In Out Coordinator
Data in is being sampled when valid is high
Data out is being sent out according to width_out_generic
DATA IN
DATA IN VALID
DATA OUT VALID
DATA OUT

## Slide 18: Simulations
At first we made a manual simulation to each entity to check the functionality
Afterwards, we built a core test bunch in order to check the entire core
Internal
Logic
Analyzer
Core
WBM
WBS

## Slide 19: Simulations
Check for | Simulation number | Check for | Simulation number
Configurations timing | 10. | Configurations, Trigger recognition | 1.
Enable polarity | 11. | Recording depth, Configurations | 2.
Reset polarity | 12. | Number of signals, Trigger position | 3.
Signal RAM width | 13. | Configurations, Reset | 4.
Input data = WB bus | 14. | Reset | 5.
Input data < WB bus | 15. | Configurations | 6.
Input data > WB bus, Reset, Configuration | 16. | Configurations | 7.
Input data >> WB bus, Reset, Configuration | 17. | Configurations, Second trigger rise | 8.
 |  | Configurations timing | 9.
Each diagram was checked and confirmed for the correct result and if necessary, code changes was made and the simulation was made again.
?

## Slide 20: Simulations
Number of signals is 5, meaning our input data is between 0-32 in decimal (2^5), at first the trigger position is 100 and all the data is recorded before the trigger, and second time the position is 0 and all the data is recorded after the trigger.
For example: (test number 3)
value | Name | #
1 | reset_polarity_g | 1
1 | enable_polarity_g | 2
3 | signal_ram_depth_g | 3
8 | signal_ram_width_g | 4
3 | record_depth_g | 5
8 | data_width_g | 6
8 | Add_width_g | 7
5 | num_of_signals_g | 8
0 | power2_out_g | 9
1 | power_sign_g | 10
6 | Type_d_g | 11
1 | Len_d_g | 12
Data is insert to the registers, in order to configure the user trigger position and type
Enable signal is written to the register to enable the system

## Slide 21: Simulations
Data is being save in the RAM until trigger rise
Since position is 100, we do not save data after trigger rise
Write controller is finish
Read controller starting to send the relevant data out
After that all the relevant data has being sent out, read controller finish working
We can now configure a new and different simulation

## Slide 22: Simulations
Since position is 0, all the data is recorded after trigger rise
After WC finish saving all the data, the RC is starting to extract the data and send it out
Read controller is extractiong all the 8 samples, starting from 24 (trigger rise)
When finish, read controller finish signal is rise, and the system is ready for another configuration

## Slide 23: Problems & Solutions
Solution | Problem
Adding entity that “break” the data into few clock cycles (data coordinator) | Coordinate between number of recorded signals to output width (WB bus width)
Inserting wc_finish signal to the registers entity and resetting the relevant register after first trigger rise | Trigger was rise twice in the same configuration
We set each register size to 7 bit and we assume that the WB bus width is larger then that. According to that we read only the 7 LSB of the data into the registers | Coordinate between incoming data width (from WBS) to the registers
Coordinate addresses of incoming data and data sent to RAM | Coordinate between input - saved data and address. (couple of clock cycles delay between them)
Will be solved in 2nd part | System can now work in clock frequency of ~50 MHZ (100 MHZ demanded)

## Slide 24: Problems & Solutions
First example: (problem that occurred in the middle presentation)
After first trigger rise, the system identify another trigger rise although the data was still recorded
Problem- there was no dependency between two trigger rises
Our solution- adding wc_finish signal to the registers and resetting the enable register

## Slide 25: Problems & Solutions
Second example: output width (bus) did not match the input width
DATA OUT
DATA OUT VALID
IN OUT COOARDINATOR
DATA OUT
DATA OUT VALID
Input width is num_of_signals_g, output width is data_width_g
Problem- the two widths don’t match
Our solution- adding an entity who coordinate between them

## Slide 26: Part B- work plan
Creating Signal Generator
Integration with external blocks (rx/tx path, WB intercon and others)
Simulations to the whole system
Synthesis
Building and connecting the GUI
Connecting to FPGA in the lab

## Slide 27
Schedule
Tasks | Date | #
Part A final presentation | 6.10.13 | 1
Submitting project documentation | 13.10.13 | 2
Finishing signal generator | 15.10.13 | 3
Integrating system blocks | 5.11.13 | 4
Top simulations | 12.11.13 | 5
synthesis | 17.11.13 | 6
Simple matlab GUI implementation | 21.11.13 | 7
Hardware burning to FPGA | 28.11.13 | 8
Part B final presentation | 6.12.13 | 9
0.5
חן