## Slide 1
IDLE
Set config
Write Controller work
RESET = 0
RESET = 1
Read Controller work
Get config
wc_is_config = 1
write_controller_finish= 0
write_controller_finish= 1
Read_controller_finish= 0
Read_controller_finish= 1
wc_is_config = 0

## Slide 2: Output table
din_valid | start_array_row_out | start_addr_out | write_controller_finish | addr_out_to_RAM | Data_out_of_wc | Output Stste
000 | 0 | 000 | 0 | 000 | 00000000 | Idle
Reading from the registers trigger_type and trigger_position and update trigger type\position signals |  |  |  |  |  | set_configurations
Waiting for enable to rise, after that the WC will start to read the data and save it in the RAM |  |  |  |  |  | wait_for_enable_rise
Save incoming data and trigger in signals |  |  |  |  |  | get_new_data_and_trigger
Check trigger signal for trigger rise according configuration that was saved in trigger position\type signals |  |  |  |  |  | check_for_trigger_rise
Enable RAM | - | - | - | Current address | Current data | send_out_data_and_addr
Check according all_data_rec_count_s if all the data is recorded after trigger rise. If so continue to send_start_addr_to_rc State, if not continue to calc_next_addr_for_data state. |  |  |  |  |  | check_if_all_data_recorded
Update current_address_s , current_row_s, din_valid_s |  |  |  |  |  | calc_next_addr_for_data
- | Start row | Start address | - | - | - | send_start_addr_to_rc
Calculate the start address and row of the data that is relevant to the user and send it to the RC |  |  |  |  |  | 
- | - | - | 1 | - | - | write_controller_is_finish