## Slide 1: Internal Logic Analyzer Final presentation-part B
By: Moran Katz and Zvika Pery
Mentor: Moshe Porian
Dual-semester project
Spring 2012

## Slide 2: Agenda
Overview
Goals
Requirements
Architecture
Internal Logic Analyzer Core
Integration
Data Flow
Simulations
Working Systems
Problems & Solutions
What have we learned

## Slide 3: Project Overview
Altera- Signal Tap
Xilinx- Chip Scope
Logic Analyzer- Debugging tool for FPGA
Contains software & hardware
Hardware: Change FPGA code
Memories to store data
Logic to change configuration
Software: Include GUI
Choose trigger, data location, signals name, record results
Common Logic Analyzer tools today:
Notes: 1.יצרניות ה- FPGA-ים מספקות כלי למטרת DEBUG במעבדה, הקרוי Logic Analyzer, המאפשר הקלטה של מידע פנימי ב- FPGA והצגתו למשתמש. הכלי בנוי מחבילת חומרה, וחבילת תוכנה.(תמונה)
2. החלק החומרתי נכנס לקוד של ה- FPGA וכולל זיכרונות לאחסון המידע המוקלט, לוגיקה לשינוי קונפיגורציה (לדוגמא: סוג ה- Trigger, לדוגמא: פעיל בשינוי מ- '0' ל- '1'), לוגיקה לזיהוי נעילה של ה- Trigger הרצוי ולוגיקה לשליחת המידע המוקלט לתוכנה.
3. החלק התוכנתי כולל GUI, המאפשר לבחור את סוג ה- Trigger להקלטה, מיקום ה- Trigger ביחס למידע המוקלט, הצגה נוחה של שמות הסיגנלים המוקלטים והצגה של תוצאות ההקלטה, המגיעות מהחומרה, למשתמש.
4. הכלי של יצרנית ה- FPGA-ים, ALTERA, נקרא SignalTap. הכלי של יצרנית ה- FPGA-ים, XILINX, נקרא ChipScope.

## Slide 4: Project goals
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Design an internal logic analyzer to the FPGA which will be an independent part
Hardware:
(1) VHDL
(2) Record the chosen signals
(3) Send it back to the user
Software:
(1) GUI- allow to present the recorded information
(2) Send request to change hardware according user’s choise
(3) Build a system to check our implementation
XILINX- SPARTAN 3E
ALTERA- CYCLON II
Altera Cyclone II
Notes: בניית Logic Analyzer פנימי ל- FPGA, בלתי תלוי ביצרן ה- FPGA. החלק החומרתי יכלול בניית מערכת ב- VHDL, המאפשרת הקלטה של הסיגנלים הרצויים ע"פ קונפיגורציה ושליחת המידע המוקלט חזרה למשתמש. החלק התוכנתי יכלול בניית GUI המאפשר שינוי קונפיגורציה והצגת המידע המוקלט למשתמש. בנוסף, תבנה מערכת תומכת המאפשרת בדיקה של המימוש במעבדה.

## Slide 5: Requirements
Save and load settings
Option to choose the parameters
Save the recorded information and present it using waveform
Internal communication is through Wishbone protocol
External communication is through UART protocol
Type of trigger, for example ‘rise’
Signals name, which signals to record
position of trigger
30%-70%
50%-50%
70%-30%
Duration of recording
Notes: כלי ה- Logic Analyzer יהיה בעל תכונות המאפשרות:
  בחירת סוג ה- Trigger: שינוי מ- '0' ל- '1' (rise), fall, '0', '1'.
  בחירת מיקום ה- Trigger ביחס למידע המוקלט (באמצע, בהתחלה, בסוף...).
  קביעת כמות הסיגנלים להקלטה.
  קביעת עומק ההקלטה (זמן ההקלטה).
  שמירת וטעינת settings של פרויקט.
  שינוי שמות הסיגנלים המוצגים.
  שמירת המידע המוקלט לקובץ והצגתו באמצעות waveform בכלי סימולציה (ב- Modelsim).
  שימוש ב- Resources (זכרונות ולוגיקה) בלתי תלויים בסוג ה- FPGA.
  אופציונאלי: הגדרת Trigger-ים חכמים, כמו Trigger מקונן (sequence של תנאים), Trigger הכולל השוואות לוגיות (greater than, לדוגמא).
כל הבלוקים ב- FPGA יקושרו ביניהם באמצעות ממשק אחיד – Protocol Wishbone.
הממשק ביו החומרה ל- GUI ולתוכנה יהיה באמצעות פרוטוקול UART.
בניית מערכת תומכת, הכוללת חומרה ותוכנה, המאפשרת הזרקת חבילות מידע, המייצגות סצנות שונות של סיגנלים להקלטה ל- FPGA, קבלת מענה ממנו בנוגע למידע המוקלט והשוואה ביחס למצופה.
הרחבה לגבי פרוטוקולי התקשורת תינתן בהמשך המצגת.

## Slide 6: Top Architecture
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Altera Cyclone II

## Slide 7: The Core
The core tasks:
Getting and saving user configurations
Getting new data each clock cycle and saving it
Getting new trigger signal each clock cycle and check for trigger rise according user configurations
Outputting relevant data back to user
The core is build from 7 entities:
WBS
Registers
Write Controller
RAM
Read Controller
Data Coordinator
WBM

## Slide 8: The Core
Description | Name | #
Generic table
1
2
3
4
5
6
7
8
9
10
11
12
reset_polarity_g
enable_polarity_g
signal_ram_depth_g
signal_ram_width_g
record_depth_g
data_width_g
Add_width_g
num_of_signals_g
power2_out_g
power_sign_g
type_d_g
len_d_g
0 - Reset active Low, 1- Reset active High
0 - Enable active Low, 1- Enable active High
depth of basic RAM
width of basic RAM
number of bits that is recorded from each signal
defines the width of the data lines of the system
width of address word in the RAM (Gets record_depth_g)
number of signals that will be recorded simultaneously
RAM output width is multiplied by this power factor
'-1' => RAM output width > input width
'1' => RAM input width > output width
Type Depth. type is the WB client which the data is directed to
Length of the WB data (in words)

## Slide 9: Integration
Platform Changes:
Changing address width in all entities
Changing number, order and addresses of WhishBone entities and making them generics
Notes: הצגת השינויים שבוצעו ברכיבים מפרויקטים אחרים: שינוי ראשון- רוחב הכתובת של המערכת וכל הישויות בה (קביעה כג'נריק). שינוי שני- התאמת רכיב OUTPUT_BLOCK והתאמתו ליציאת רכיב הCORE (חיבור בפרוטוקול WISHBONE)

## Slide 10: Data Flow
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Trigger- first signal
Recording time- 50%
Signal’s number-2
injecting signals behavior
signal
signal
signal
Recorded data
Altera Cyclone II
Notes: קביעת קונפיגורציות: לדוגמא נבחר כטריגר סיגנל ראשון, עם עומק הקלטה של 50%

## Slide 11: Simulations
At first we made a manual simulation to each entity to check the functionality
Afterwards, we built a top test bunch in order to check the entire system
Internal
Logic
Analyzer
Core
WBM
WBS

## Slide 12: Working Systems
File sharing- via SVN
Coding Guidelines- code design according known conventions, usage of entity template
Code Review- 1. Visual/ Compiler
            2. Local simulation to the entity
            3. Top simulation

## Slide 13: Problems & Solutions
Solution | Problem
Adding entity that “break” the data into few clock cycles (data coordinator) | Coordinate between number of recorded signals to output width (WB bus width)
Inserting wc_finish signal to the registers entity and resetting the relevant register after first trigger rise | Trigger was rise twice in the same configuration
We set each register size to 7 bit and we assume that the WB bus width is larger then that. According to that we read only the 7 LSB of the data into the registers | Coordinate between incoming data width (from WBS) to the registers
Coordinate addresses of incoming data and data sent to RAM | Coordinate between input - saved data and address. (couple of clock cycles delay between them)
Changing the inputs of the entity and connect it via whishbone protocol | Output block incoming data doe’s not compatible to whishbone protocol

## Slide 14: Problems & Solutions
First example: (problem that occurred in the middle presentation)
After first trigger rise, the system identify another trigger rise although the data was still recorded
Problem- there was no dependency between two trigger rises
Our solution- adding wc_finish signal to the registers and resetting the enable register

## Slide 15: Problems & Solutions
Second example: output width (bus) did not match the input width
DATA OUT
DATA OUT VALID
IN OUT COOARDINATOR
DATA OUT
DATA OUT VALID
Input width is num_of_signals_g, output width is data_width_g
Problem- the two widths don’t match
Our solution- adding an entity who coordinate between them