## Slide 1: Internal Logic Analyzer Middle presentation-part A
By: Moran Katz and Zvika Pery
Mentor: Moshe Porian
Dual-semester project
Spring 2012

## Slide 2: Agenda
Overview
Goals
Requirements
Architecture
Data transfer
Internal Logic Analyzer Core
Generics
Registers
Write controller
Read controller
RAM
Simulations
Schedule

## Slide 3: Project Overview
Altera- Signal Tap
Xilinx- Chip Scope
Logic Analyzer- Debugging tool for FPGA
Contains software & hardware
Hardware: Change FPGA code
Memories to store data
Logic to change configuration
Software: Include GUI
Choose trigger, data location, signals name, record results
Common Logic Analyzer tools today:
Notes: 1.יצרניות ה- FPGA-ים מספקות כלי למטרת DEBUG במעבדה, הקרוי Logic Analyzer, המאפשר הקלטה של מידע פנימי ב- FPGA והצגתו למשתמש. הכלי בנוי מחבילת חומרה, וחבילת תוכנה.(תמונה)
2. החלק החומרתי נכנס לקוד של ה- FPGA וכולל זיכרונות לאחסון המידע המוקלט, לוגיקה לשינוי קונפיגורציה (לדוגמא: סוג ה- Trigger, לדוגמא: פעיל בשינוי מ- '0' ל- '1'), לוגיקה לזיהוי נעילה של ה- Trigger הרצוי ולוגיקה לשליחת המידע המוקלט לתוכנה.
3. החלק התוכנתי כולל GUI, המאפשר לבחור את סוג ה- Trigger להקלטה, מיקום ה- Trigger ביחס למידע המוקלט, הצגה נוחה של שמות הסיגנלים המוקלטים והצגה של תוצאות ההקלטה, המגיעות מהחומרה, למשתמש.
4. הכלי של יצרנית ה- FPGA-ים, ALTERA, נקרא SignalTap. הכלי של יצרנית ה- FPGA-ים, XILINX, נקרא ChipScope.

## Slide 4: Project goals
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Design an internal logic analyzer to the FPGA which will be an independent part
Hardware:
(1) VHDL
(2) Record the chosen signals
(3) Send it back to the user
Software:
(1) GUI- allow to present the recorded information
(2) Send request to change hardware according user’s choise
(3) Build a system to check our implementation
XILINX- SPARTAN 3E
ALTERA- CYCLON II
Altera Cyclone II
Notes: בניית Logic Analyzer פנימי ל- FPGA, בלתי תלוי ביצרן ה- FPGA. החלק החומרתי יכלול בניית מערכת ב- VHDL, המאפשרת הקלטה של הסיגנלים הרצויים ע"פ קונפיגורציה ושליחת המידע המוקלט חזרה למשתמש. החלק התוכנתי יכלול בניית GUI המאפשר שינוי קונפיגורציה והצגת המידע המוקלט למשתמש. בנוסף, תבנה מערכת תומכת המאפשרת בדיקה של המימוש במעבדה.

## Slide 5: Requirements
Save and load settings
Option to choose the parameters
Save the recorded information and present it using waveform
Internal communication is through Wishbone protocol
External communication is through UART protocol
Type of trigger, for example ‘rise’
Signals name, which signals to record
position of trigger
30%-70%
50%-50%
70%-30%
Duration of recording
Notes: כלי ה- Logic Analyzer יהיה בעל תכונות המאפשרות:
  בחירת סוג ה- Trigger: שינוי מ- '0' ל- '1' (rise), fall, '0', '1'.
  בחירת מיקום ה- Trigger ביחס למידע המוקלט (באמצע, בהתחלה, בסוף...).
  קביעת כמות הסיגנלים להקלטה.
  קביעת עומק ההקלטה (זמן ההקלטה).
  שמירת וטעינת settings של פרויקט.
  שינוי שמות הסיגנלים המוצגים.
  שמירת המידע המוקלט לקובץ והצגתו באמצעות waveform בכלי סימולציה (ב- Modelsim).
  שימוש ב- Resources (זכרונות ולוגיקה) בלתי תלויים בסוג ה- FPGA.
  אופציונאלי: הגדרת Trigger-ים חכמים, כמו Trigger מקונן (sequence של תנאים), Trigger הכולל השוואות לוגיות (greater than, לדוגמא).
כל הבלוקים ב- FPGA יקושרו ביניהם באמצעות ממשק אחיד – Protocol Wishbone.
הממשק ביו החומרה ל- GUI ולתוכנה יהיה באמצעות פרוטוקול UART.
בניית מערכת תומכת, הכוללת חומרה ותוכנה, המאפשרת הזרקת חבילות מידע, המייצגות סצנות שונות של סיגנלים להקלטה ל- FPGA, קבלת מענה ממנו בנוגע למידע המוקלט והשוואה ביחס למצופה.
הרחבה לגבי פרוטוקולי התקשורת תינתן בהמשך המצגת.

## Slide 6: Architecture
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Altera Cyclone II

## Slide 7: Data Transfer
UART IN
RX PATH
WBM
WhishBone
intercon
Signal
Generator
Internal
Logic
Analyzer
Core
WBM
WBS
TX PATH
WBM
WBS
UART OUT
Clock &
Reset
100 MHZ
Reset
50 MHZ
GUI
FPGA
Reset
WBS
WBM- Whishbone Master
WBS-Whishbone Slave
Trigger- first signal
Recording time- 50%
Signal’s number-2
injecting signals behavior
signal
signal
signal
Recorded data
Altera Cyclone II
Notes: קביעת קונפיגורציות: לדוגמא נבחר כטריגר סיגנל ראשון, עם עומק הקלטה של 50%

## Slide 8: The Core
Internal
Logic
Analyzer
Core
WBM
WBS
The core have 6 sub blocks:
Write controller.
Read controller.
Registers.
RAM.
WBS.
WBM.

## Slide 9: Generics
Defult Value | Type | Description | Generic Parameter | Number
256 | Positive | Determine the number of bits that will be recorded for each signal | Record_depth_g | 1.
8 | Positive | Determine the number of signals that will be recorded | Num_of_signals_g | 2.
'1' | Std_logic | Reset polarity: '1': Active high '0':Active low | Reset_polarity_g | 3.
'1' | Std_logic | Enabling the system: '1': Active high '0':Active low | Enable_polarity_g | 4.
8 | Positive | The Width of the basic 'word' of wishbone interface | Data_width_g | 5.
8 | Positive | The address Width of wishbone interface | Add_width_g | 6.
10 | Positive | Number of lines in the basic RAM used in the core | Signal_ram_depth_g | 7.
8 | Positive | The Width of the basic 'word' of the basic RAM used in the core | Signal_ram_width_g | 8.
3 | Positive | Address Depth | addr_d_g | 9.
1 | Positive | Length Depth | len_d_g | 10.
1 | positive | Type Depth | type_d_g | 11.
The generics contains the basic values of the core’s parts and the configurations of the user.
The generics stay steady during the whole time.
Notes: ה GENERICS הם גדלים אשר מגדירים לנו את המערכת.
הם מוגדרים פעם אחת בתחילת ריצת התוכנית ונשמרים לכל אורכה.
לא ניתן לשנות את גדלי הGENERICS תוך כדי ריצת התוכנית.
חלקם מוגדרים ע"י המשתמש וחלקם מוגדרים ע"י המערכת (מוגדרים בזמן התכנון, בקוד)

## Slide 10: Registers
In the project we have four units of registers:
Trigger type – values between 0-3. defines the type of trigger that we are looking for- {rise, fall, one or zero (for 3 cycles)}.
Trigger position- get values between 0-100. the percentage of the data that will recorded before trigger rise.
clk to start- values 0-256. Saves the number of clock cycles since the system was enabled until trigger rise.
Enable- values 0 or 1. The status of the system, meaning our core starts looking for trigger rise.
First we receive the configurations from the user.
we than change the Enable to ‘1’.
At the end, after we have found trigger rise we update Clk to start in every cycle.
“000”
“001”
“001”
“11001”
“011”
“1”
“010”
1+
Notes: יחידת הרגיסטרים-תפקידה לשמור מספר נתונים אשר משמשים את חלקי הליבה השונים. זוהי יחידת זיכרון זמינה ואמינה אשר משמשת לשמירת מידע התחלתי על קונפיגורצית המשתמש(TRIGG TYPE,TRIGG POSITION) ומידע עזר לדיבוג(CLK TO START).
קיימים אצלנו (בינתיים) 4 רגיסטרים, כאשר ישנה אופציה להוסיף עוד לפי הצורך.

## Slide 11: Write controller
The inputs are the configurations from the registers, and the trigger.
The outputs are the addresses of the relevant data(according to the configuration).
The write controller calculates the address of the relevant data and send it to the read controller .
The Blocks Diagram
In every cycle we get a new trigger and data.
The WC calc the current address and sends it to the RAM.
ALU trigger compare the trigger signal to the relevant configuration.
In case we find a trigger rise, we rise the “trigger found” signal for one cycle.
New Trigger
New Data
Cuurent addr
Cuurent addr
Next addr
Trigger Position
Trigger Type
Str addr\ed addr
‘1’

## Slide 12: Read controller
Recieves a start and an end address of the relevant data, that needs to be sent back to the user.
Recieves the data from the RAM and send it to the user via the WBM.
The Block Diagram
Starts according to trigger rise.
The start and end addresses are being saved, and in every cycle the relevant address is sent to the RAM.
In parallel, data is coming from the RAM and being sent out to the user.
‘0’ -> ‘1’
Data from the RAM
START\END ADDR
START\END ADDR
Next addr out
Notes: ה-RC מקבל את כתובת ההתחלה והסיום של המידע הרלבנטי שצריך להשלח חזרה למשתמש. בכל מחזור שעון, נשלחת כתובת של מידע ל-RAM, ומתקבלת "מילה" מה-RAM.

## Slide 13: RAM
The main memory unit.
All the data that’s come as input and needed to be send back to the user is saved in the RAM between that.
The RAM size is determined according the relevant generics-
For example:
Record_depth_g = 4,
Num_of_signals_g = 5,
Signal_ram_depth_g = 3,
Signal_ram_width_g = 3.
Ram width |  |  | 
s1 | s1 | s1 | Ram depth
s2 | s2 | s2 | 
s3 | s3 | s3 | 
Ram width |  |  | 
Φ | Φ | s1 | Ram depth
Φ | Φ | s2 | 
Φ | Φ | s3 | 
Ram width |  |  | 
s4 | s4 | s4 | Ram depth
Φ | Φ | Φ | 
Φ | Φ | Φ | 
Ram width |  |  | 
Φ | Φ | s4 | Ram depth
Φ | Φ | Φ | 
Φ | Φ | Φ | 
Input cycle:
Getting the input addtess and data to save.
Saving the data in the RAM.
Address enable currect RAM
Input data
Enable correct RAM
output address
'1'
'0'
Output cycle:
Sending the output address to the RAM.
The output is the relevant data and the valid signal.
Enable correct RAM
'0'
‘1’
Output data
Valid output
First signal
First “word”

## Slide 14: Simulations
The simulations were done manually in ModelSim.
Generics are at default Values and the input signals were changed in order to check the output.
Test 1:
trigger rise.
trigger position is 0.

## Slide 15
Notes: עיגולים אדומים- עליית טריגר.
ריבוע טורקיז- מראה את הכתובות שנשלחות לחלקים השונים. כתובת נוכחית שנשלחת לRAM, כתובת מתאימה שנשלחת לREAD CONTROLLER- בקונפיגורציה הנוכחית אנו שומרים את כל המידע מעליית טריגר ואילך (trigger position = 0), כלומר הכתובת הראשונה תהיה אחת לפני הכתובת הנוכחית שנשלחת לRAM (המידע החדש שהגיע מקבל כתובת זו, כלומר המידע שהגיע בעליית השעון הקודמת ובו בוצעה עליית הטריגר הוא כתובת אחת לפני) וכתובת הסיום תהיה תמיד אחד לפני כתובת ההתחלה שנשלחת ל RC (אנו מגדירים תמיד גודל RAM עבור מספר הדגימות שאנו צריכים לדגום, כלומר אם יש לנו את כתובת ההתחלה נחסיר ממנה כתובת אחת ונקבל את כתובת הסיום).

## Slide 16: Simulations
Test 2:
trigger types:
First trigger is fall.
Second trigger is ones.

## Slide 17
Schedule
Tasks | Date | #
Finishing Read controller code+simulations. | 15.5.13 | 1
connecting core parts. | 20.5.13 | 2
Matlab GUI implementation | 15.6.13 | 3
Top simulations | 30.6.13 | 4
Hardware burning to FPGA | 7.7.13 | 5
Lab validation tests | 15.7.13 | 6
End of first semester Presentation | 30.7.13 | 7
Adding smart triggers | 15.8.13 | 8
Testing new triggers | 22.8.13 | 9
End of second semester Presentation | 1.9.13 | 10
0.5
חן